## Slide 1: 車載監控系統
指導老師 : 陳朝烈 analysis
組員 : 葉日勝 黃柏儒 黃少鏞 楊豐瑞

## Slide 2: OUTLINE
功能分析
資料流分析
活動分析
1
2
3

## Slide 3
駕駛者:
  可透過螢幕看到三個方位影像，並且上傳雲端。
  MCU會接受到管理者指示警告駕駛者不良駕駛行為。
雲:
  接收到三方圖片做縫合處裡
  妥善分配運算資源
管理者:
  以環景的方式投射在UI上，監視駕駛者行為模式
  下達警告指令
CAMERA
RASPBERRY
UDP
UI
UDP
MQTT
MCU
M
功能分析
1

## Slide 4
資料流分析
2

## Slide 5
資料流分析
2

## Slide 6: udp
Input:
Output:
Method:

## Slide 7: MQTT
Input:
Output:
Parameter:
Method:

## Slide 8: mcu
Input:
  Image1, Image2, Image3
Output:
  Image[3]{Image 1, Image 2, Image 3}
Parameter: null
Method:
  由USB輸入3個方向影像，存入陣列，由UDP(4G)傳送

## Slide 9: rsp1
Input:
  Image[3]{Image 1, Image 2, Image 3}
Output:
  對應raspberry，由MQTT輸出
    傳送Image[1], Image[2] =>RSP2
    傳送Image[2], Image[3] =>RSP3
Parameter:
  ID:樹梅派ID
  Image[]:影像內容
Method:
  Send Image(image[], ID); //由MQTT傳送到指定的raspberry
    Ex: Send Image(image[1] [2], RSP2);

## Slide 10: rsp2
Input:
  Image[1], Image[2]
Output:
  Result1
Parameter:
Method:
  ImageKP KeyPointDetector(Image)
  ImageFE FeatureExtraction(ImageKP)
  ImageFM FeatureMatching(ImageFE)
  Image[1]: ImageA1 Affine(ImageFM) / Image[2]: ImageA2 Affine(ImageFM)
  Result1 Stitch(ImageA1, ImageA2)

## Slide 11: rsp3
Input:
  Image[2], Image[3]
Output:
  Result2
Parameter:
Method:
  ImageKP KeyPointDetector(Image)
  ImageFE FeatureExtraction(ImageKP)
  ImageFM FeatureMatching(ImageFE)
  Image[2]: ImageA1 Affine(ImageFM) / Image[3]: ImageA2 Affine(ImageFM)
  Result2 Stitch(ImageA1, ImageA2)

## Slide 12: rsp4
Input:
  Result1, Result2
Output:
  Result3
Parameter:
Method:
  ImageKP KeyPointDetector(Image)
  ImageFE FeatureExtraction(ImageKP)
  ImageFM FeatureMatching(ImageFE)
  Result1: ImageA1 Affine(ImageFM) / Result2 : ImageA2 Affine(ImageFM)
  Result3 Stitch(ImageA1, ImageA2)

## Slide 13: ui
Input: Result3
Output:
Parameter:
Method:

## Slide 14
CAM1
Catch
R_Photo
CAM2
Catch
M_Photo
CAM3
Catch
L_Photo
1.R_Photo
1. M_Photo
1. L_Photo
MCU
Read image-data
Show and Send image
USB
HOST
WiFi
4G/5G
UDP
USB
HUB
2.
R_Photo
M_Photo
L_Photo
RSP1
Get image source
Distribute photos
MQTT
Publish
Broker
RSP3
Stitch photo
(M) (L)
MQTT
Subscriber
RSP2
Stitch photo
(R) (M)
MQTT
Subscriber
3.
R_Photo
M_Photo
3.
M_Photo
L_Photo
MQTT
RSP4
Stitch photo
(R-M) (M-L)
MQTT
Subscriber
4.
M-L_Photo
4.
R-M_Photo
UI
Display
Video
Surveillance
5.
(R-M-L)Photo
Ethernet
640*480
640*480
1040*480
1480*480
UDP

## Slide 15
Input: R_Photo M_Photo L_Photo
Output: Photo(R,M,L)
Method: cap.VideoCapture() UDP_send
Input: Photo(R,M,L)
Output(Path): R_Photo(RSP2) M_Photo(RSP2、3) L_Photo(RSP3)
Method: MQTT_Distribute
Input: R_Photo M_Photo
Output: (R-M)Photo
Parameter: R_Photo[0:200,:] M_Photo[440:640,:]
Method: SURF Affine Transform Stitch by Blending
Input: (R-M)Photo (M-L)Photo
Output: (R-M-L)Photo
Parameter: (R-M)Photo[0:640,:] (M-L)Photo[640:1280,:]
Method: SURF Affine Transform Stitch by Blending
Input: M_Photo L_Photo
Output: (M-L)Photo
Parameter: M_Photo[0:200,:] L_Photo[440:640,:]
Method: SURF Affine Transform Stitch by Blending
MCU
RSP

## Slide 16
資料流分析
2
Step1:UDP收取車輛傳輸的3個角度照片(照片1 2 3)，並利用MQTT分送至3個node(node1 2 3)做分散式運算
Step2:node同步收取照片後找出keypoints
Step3:node2找出的keypoints丟至node1及node3
Step4:node1將照片1、2合併node3將照片2、3合併
Step5:做affine並丟回Master
Step6:合併node1及node2合併的照片變成一張廣角圖
Final：利用UDP丟至行控中心的UI段端進行監控

## Slide 17
活動分析
3