## Slide 1: 車載監控系統
指導老師 : 陳朝烈
組員 : 葉日勝 黃柏儒 黃少鏞 楊豐瑞

## Slide 2: OUTLINE
功能分析
資料流分析
活動分析
1
2
3

## Slide 3
駕駛者:
  可透過螢幕看到三個方位影像，並且上傳雲端。
  MCU會接受到管理者指示警告駕駛者不良駕駛行為。
雲:
  接收到三方圖片做縫合處裡
  妥善分配運算資源
管理者:
  以環景的方式投射在UI上，監視駕駛者行為模式
  下達警告指令
CAMERA
RASPBERRY
UDP
UI
UDP
MQTT
MCU
M
功能分析
1

## Slide 4
資料流分析
2

## Slide 5
資料流分析
2
L
M
R
L
M
R
L
M
R
R
L
M
L
R
L
R
M
M
M

## Slide 6
資料流分析
2

## Slide 7: Udp(被監控端)
Udp(監控端)
INPUT
L_Photo
M_Photo
R_Photo
INPUT
(L-M-R)Photo
METHOD
使用Socket搭建Ethernet，為了可以加強傳送的即時性，以UDP方式對傳輸端傳送。

## Slide 8: mcu
OUTPUT
Image[3]
{L_Photo,
M_Photo,
R_Photo}
PARAMETER
Null
METHOD
由USB輸入3個方向影像，存入陣列，由UDP(4G)傳送
INPUT
L_Photo
M_Photo
R_Photo

## Slide 9: Rsp1 (Distribute photo)
PARAMETER
Topic
(MQTT Topic)
METHOD
Send Image(image[],Topic);
INPUT
Image[3]
{L_Photo,
M_Photo,
R_Photo}
Image[]
(影像內容)
OUTPUT
M_Photo,
R_Photo
To RSP2
OUTPUT
L_Photo,
M_Photo
To RSP3
//由MQTT傳送到指定的raspberry
Read Image[];

## Slide 10: Rsp2 (Stitch photo)
OUTPUT
M-R_Photo
METHOD
KeyPoints Detector – data array
Feature Extraction – data array
Feature Matching - image
Affine - image
Stitch - image
INPUT
M_Photo
R_Photo
PARAMETER
Topic
(MQTT Topic)
Image[]
(影像內容)

## Slide 11: Rsp3 (Stitch photo)
OUTPUT
L-M_Photo
INPUT
L_Photo
M_Photo
PARAMETER
Topic
(MQTT Topic)
Image[]
(影像內容)
METHOD
KeyPoints Detector – data array
Feature Extraction – data array
Feature Matching - image
Affine - image
Stitch - image

## Slide 12: Rsp4 (Stitch photo)
OUTPUT
L-M-R_Photo
PARAMETER
Null
INPUT
M-R_Photo
L-M_Photo
METHOD
KeyPoints Detector – data array
Feature Extraction – data array
Feature Matching - image
Stitch - image

## Slide 13: MQTT
為降低雲溝通的流失，所以選擇QOS2的方式搭建。
METHOD
INPUT
Topic 1 : M_Photo, R_Photo
Topic 2: L_Photo, M_Photo
Topic 3 : M-R_Photo
Topic 4 : L-M_Photo
PARAMETER
Topic
OUTPUT
Topic 1 : M_Photo, R_Photo
Topic 2: L_Photo, M_Photo
Topic 3 : M-R_Photo
Topic 4 : L-M_Photo

## Slide 14: ui
OUTPUT
顯示影像
(VGA or HDMI)
PARAMETER
Null
METHOD
UDP接受資料，透過C# Form呈現介面，畫面藉由VGA or HDMI
INPUT
L-M-R_Photo

## Slide 15
CAM1
Catch
R_Photo
CAM2
Catch
M_Photo
CAM3
Catch
L_Photo
1.R_Photo
1. M_Photo
1. L_Photo
MCU
Read image-data
Show and Send image
USB
HOST
WiFi
4G/5G
UDP
USB
HUB
2.
R_Photo
M_Photo
L_Photo
3.
R_Photo
M_Photo
3.
M_Photo
L_Photo
MQTT
RSP4
Stitch photo
(R-M) (M-L)
4.
L-M_Photo
4.
M-R_Photo
UI
Display
Video
Surveillance
Ethernet
640*480
640*480
1080*480
1520*480
UDP
RSP3
Stitch photo
(M) (L)
Subscriber
RSP1
Get image source
Distribute photos
Publish
Stitch photo
(R) (M)
Subscriber
RSP2
Broker
Broker
5.
(L-M-R)Photo
S
U
B
S
C
R
I
B
E
R
Broker
Publish
Publish

## Slide 16
Input: R_Photo M_Photo L_Photo
Output: Photo(R,M,L)
Method: cap.VideoCapture() UDP_send
Input: Photo(R,M,L)
Output(Path): R_Photo(RSP2) M_Photo(RSP2、3) L_Photo(RSP3)
Method: MQTT_Distribute
Input: R_Photo M_Photo
Output: (R-M)Photo
Parameter: R_Photo[0:200,:] M_Photo[440:640,:]
Method: SURF Affine Transform Stitch by Blending
Input: (R-M)Photo (M-L)Photo
Output: (R-M-L)Photo
Parameter: (R-M)Photo[0:640,:] (M-L)Photo[640:1280,:]
Method: SURF Affine Transform Stitch by Blending
Input: M_Photo L_Photo
Output: (M-L)Photo
Parameter: M_Photo[0:200,:] L_Photo[440:640,:]
Method: SURF Affine Transform Stitch by Blending
MCU
RSP

## Slide 17
資料流分析
2
Step1:UDP收取車輛傳輸的3個角度照片(照片1 2 3)，並利用MQTT分送至3個node(node1 2 3)做分散式運算
Step2:node同步收取照片後找出keypoints
Step3:node2找出的keypoints丟至node1及node3
Step4:node1將照片1、2合併node3將照片2、3合併
Step5:做affine並丟回Master
Step6:合併node1及node2合併的照片變成一張廣角圖
Final：利用UDP丟至行控中心的UI段端進行監控

## Slide 18
活動分析
3